## Slide 1: Representing data in computers

## Slide 2: Binary numbers vs. denary numbers (decimal representation of numbers)
Weighting
  The raised number after the various tens/twos are called exponents
Positional notation
  A digit’s position determines its weighting
  The leftmost bit  the most-significant bit (m.s.b.)
  The rightmost bit  the least-significant bit (l.s.b.)

## Slide 3: Negative integers in binary
2’s complement system

## Slide 4: Fractions in binary
8-bit binary fractions
  0.0101000 in binary= ¼+ 1/6 =5/16= 0.3125 in denary
  The bits after the binary point in binary fraction are weighted as follows
2-1 | 2-2 | 2-3 | 2-4 | ...
½ =0.5 | ¼ = 0.25 | 1/8 = 0,125 | 1/16 = 0.0625 | ...

## Slide 5: Representing data in the PC

## Slide 6: Representing text
ASCII (American Standard Code for Information Interchange)
  7-bit code (how many characters or actions can it represent?)
  Other than 26 letters?
  Cyrillic characters?
Unicode
  16 bits, 65000+ characters
  Extension mechanism enable additional 1 million Characters to be coded
Notes: 2 to the power of 7 = 128

## Slide 7: Representing moving images
Still image as a frame
  Pixels (or pels, picture elements)
  300 pixels per inch, the size of 2 X 3 inches 256 bit colour picture = 600x900x256 bits = 540 000 bytes
Animations vs. videos
  Drawn vs. captured by camera
MPEG (motion picture expert group, a compression technique)

## Slide 8: Representing sound
Speech, music...an analogue physical quantity varies with time
Frequency
  High/low-pitched sound
  Hertz (Hz): ONE cycle per second
Sampling theorem
  How often must the sound be sampled?
    Frequencies in the sound range from 0 to B Hz, the sound must be sampled at a rate greater than 2B samples per second
MP3 (MPEG-1 Audio layer 3)

## Slide 9: Before the Next Session
Print out 4introduction_to_computational_thinking_printable.pdf